## Slide 1
A Robust Fetal ECG Detection Method for Abdominal Recordings
Reproducing and evaluating Martens et al. (2007) on the CinC 2013 dataset
Federico Cerutti - 85644A
Biomedical Signal Processing Project
Notes: Introduce the topic: detecting the fetal ECG from electrodes on the mother's abdomen, and reproducing/evaluating a well-known non-blind sequential-analysis method against a blind (ICA) baseline on a real, public dataset.

## Slide 2
Clinical motivation
▪ Fetal cardiac activity → key indicator of fetal well‑being
▪ Doppler ultrasound: routine, but gives only heart rate (FHR), not morphology
▪ Fetal ECG (FECG) also carries PR/QRS/ST morphology → linked to fetal oxygenation
▪ Abdominal FECG = non‑invasive, usable throughout pregnancy and labour (vs. invasive scalp electrode, labour‑only)
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
2
Notes: Frame why this matters clinically: Doppler ultrasound is the current standard but only gives FHR; abdominal FECG could add morphological information non-invasively, and — unlike a scalp electrode — from early pregnancy through labour, and even for long-term ambulatory/home monitoring.

## Slide 3
The core challenge
▪ FECG amplitude: tiny (tens of µV)
▪ Buried under: baseline wander, power‑line interference, EMG/motion artifacts
▪ Above all: the mother's ECG (MECG) — an order of magnitude larger, same electrodes
▪ Goal: strip away everything that isn't the fetal heartbeat
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
3
Notes: Set up the signal-processing problem: on an abdominal recording, the fetal signal is small and mixed with several much larger interferers, dominated by the mother's own ECG. Every stage of the pipeline exists to remove one of these specific interferers.

## Slide 4
Two paradigms
Blind (ICA / BSS)
Non‑blind (Sequential Analysis)
▪ No prior knowledge assumed
▪ Relies purely on statistical independence of sources
▪ As many independent sources as channels required
▪ Exploits a priori knowledge of each interferer
▪ Uses periodicity, morphology, frequency content
▪ Paper's thesis: more robust, especially at low SNR
vs.
→ This is what we test on real data in this presentation
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
4
Notes: Two philosophically different approaches exist in the literature. ICA treats the problem as pure blind source separation. The paper instead proposes exploiting what we *already know* about each interference source — its periodicity, its expected morphology — to remove them one by one. The rest of the talk tests whether that pays off.

## Slide 5
Pipeline overview
S1
Baseline Wander Remover
S2
PLI Canceller
S3
Sampling‑Rate Increaser
S4
[Maternal QRS Detector]
MECG Canceller
S5
[Fetal QRS Detector]
FECG Extractor
S6 +FHR
Note: this dataset is natively 1000 Hz (paper: 400 Hz) → upsampled to 2000 Hz for MECG cancellation precision
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
5
Notes: Walk through the five stages left to right: remove baseline wander, remove power-line interference, increase the sampling rate for precision, detect and cancel the maternal ECG, then detect and extract the fetal ECG. Flag the one dataset-driven deviation from the paper up front: native sampling here is 1000 Hz, not 400 Hz, so the upsampling step goes 1000→2000 Hz instead of 400→2000 Hz.

## Slide 6
Stage 1–2 in practice: baseline wander + power‑line interference
▪ Baseline wander: linear‑phase FIR high‑pass, 3 Hz cutoff, Hamming window — matches the paper exactly
▪ Power‑line interference: adaptive PLL‑style canceller with a QRS‑blocking mask (protects heartbeats while tracking the 50 Hz line) — same adaptive‑cancellation spirit as the paper, different mechanism
▪ Result: 50 Hz line essentially gone from the spectrum
Figure 1. baseline wander + power-line interference
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
6
Notes: The baseline wander filter is a direct, faithful implementation of the paper's design — if asked to justify the filter design itself, the backup transfer-function plot shows the expected flat 0 dB passband and a sharp roll-off right at the 3 Hz cutoff, with a clean linear phase confirming no distortion. Power-line cancellation uses a different adaptive mechanism (phase-locked-loop-style tracking with a mask that avoids distorting QRS complexes) but achieves the same goal. Point to the PSD panel on the right of the main image — the 50 Hz peak is clearly gone after processing.

## Slide 7
Stage 3–4 in practice: maternal QRS detection & MECG cancellation
▪ Maternal QRS detection: PCA channel‑combination (maximises SNR) + cross‑correlation matched filter — matches the paper
▪ MECG cancellation: average P‑wave/QRS/T‑wave templates, each scaled independently via least squares (paper's method)
▪ This implementation adds Ridge (Tikhonov) regularisation to that least‑squares fit for numerical stability — one deviation from the original paper
Figure 2. maternal QRS detection & MECG cancellation
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
7
Notes: QRS localisation follows the paper closely: combine channels via PCA to boost SNR, then find peaks by matched filtering. MECG removal also follows the paper's core idea — average and independently rescale the P, QRS and T segments to account for morphology changing over time — but this implementation regularises the least-squares fit (Ridge/Tikhonov) for stability, an addition not in the original paper. The image shows the large maternal complexes (S4) almost entirely gone after cancellation (S5).

## Slide 8
Stage 5 in practice: fetal QRS detection & FECG extraction
▪ PCA enhancement of the MECG‑free signal
▪ Candidate peaks: squared‑signal energy thresholding
▪ Refinement: cross‑correlation matched filter
▪ Final step: synchronous averaging of ~150 beats → SNR boost of √N (paper's approach)
Figure 3. fetal QRS detection & FECG extraction
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
8
Notes: With the MECG gone, the much smaller fetal QRS complexes are found the same way as the maternal ones were, but on the energy of the squared signal rather than the raw amplitude, then confirmed by matched filtering. Averaging many detected beats together — as the paper does — sharply improves the effective SNR of the extracted FECG template.

## Slide 9
Full pipeline at a glance
▪ Raw → cleaned → MECG removed → clean averaged fetal beat
▪ One figure, four stages, four channels
Figure 4. Full pipeline at a glance
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
9
Notes: This is the pipeline in one picture: S1 raw signal, S4 after baseline/power-line cleanup and upsampling, S5 after MECG cancellation, and S6 the final averaged fetal QRS morphology per channel. This is the strongest single "it works" visual in the deck — worth pausing on.

## Slide 10
Qualitative validation against ground truth
▪ Detected fetal QRS peaks (red) vs. `.fqrs` ground‑truth annotations (blue), ±50 ms tolerance
▪ Real 10‑second, 4‑channel strip
▪ Averaged fetal morphology across 124 ground‑truth‑matched beats
Figure 5. Qualitative validation against ground truth
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
10
Notes: Beyond aggregate numbers, this shows detection quality directly on real data: red detected markers line up closely with the blue ground-truth annotations across all four channels. The bottom panel shows the resulting averaged fetal beat shape built from 124 correctly matched beats — a clean, physiologically plausible QRS morphology.

## Slide 11
Baseline comparison: the ICA pipeline
▪ FastICA run on the same preprocessed data (baseline wander + PLI removed) as the "blind" alternative
▪ Best independent component auto‑selected by FHR‑detection yield
▪ Note: the paper used JADE; this implementation uses FastICA (same blind‑source‑separation family)
Figure 6. Baseline comparison: the ICA pipeline
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
11
Notes: For a controlled, apples-to-apples comparison, the same preprocessed signals are also fed through FastICA, and the independent component that yields the most valid fetal heart-rate points is picked automatically as the "best" fetal source. This substitutes FastICA for the paper's JADE algorithm — both are blind source separation methods, so the comparison stays fair in spirit.

## Slide 12
Evaluation metrics
Success = ≥60% of the recording covered by physiologically valid, RR‑interval‑derived FHR estimates
Reliability = 1 − (outliers / total), outlier = >10 bpm deviation from the 10s‑block median FHR
SNRⱼ, SIRⱼ (dB) — from S6 (averaged FECG) vs. S4−S5 (MECG) and vs. residual noise power
Precision (PPV) = TP / (TP+FP), Recall (Sensitivity) = TP / (TP+FN), F1 — matched to `.fqrs` ground truth at ±50 ms tolerance
FHR‑value MAE / RMSE (bpm) — estimated vs. ground‑truth FHR, interpolated onto a common 1 s grid
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
12
Notes: These are exactly the metrics computed in this codebase. Success and reliability follow the paper's definitions; SNR/SIR are derived per-channel from the pipeline's own intermediate signals; precision/recall/F1 come from directly matching detected peaks to the dataset's ground-truth fetal QRS annotations within a 50 ms window; MAE/RMSE instead compare the actual FHR *values* (bpm) of the two traces once interpolated onto a shared time grid — a complementary check on top of precision/recall/F1, since a method can match peak locations well but still drift on the derived heart rate, or vice versa. There's no separate classification-style "accuracy" metric here — precision/recall/F1 together with MAE/RMSE are more informative for a detection-plus-estimation task like this.

## Slide 13
Results I: success rate & reliability
▪ FHR detection success rate: Sequential Analysis 92% vs. ICA 96% (23/25 vs. 24/25 records)
▪ Mean FHR reliability (feasible records only): Sequential Analysis 0.753 vs. ICA 0.684
▪ Box plots: SA's spread is tighter and more consistent — ICA is bimodal (several near‑perfect records, several collapsed as low as ~0.23)
Figure 7. success rate & reliability
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
13
Notes: Success rate alone slightly favors ICA here (96% vs. 92% — it produces a passable trace on one more record than SA does). Reliability tells a different, more decisive story: on the records where each method *does* produce a trace, SA's is markedly more reliable on average (0.753 vs 0.684). The box plot shows why — ICA's median is actually comparable to SA's, but its distribution is bimodal: several records are detected almost perfectly, while others collapse to very low reliability (down to about 0.23), which is what pulls its mean down and its spread wide. SA sits more consistently in the mid-to-high range across records. This is the first hint that the full picture is more nuanced than any single metric — the ground-truth comparison on the next slide settles it more decisively.

## Slide 14
Results II: ground‑truth precision / recall / F1 (headline slide)
▪ Sequential Analysis: 77.4% precision / 67.1% recall / 71.9% F1
▪ ICA: 59.7% precision / 53.1% recall / 56.2% F1
▪ Matched against real `.fqrs` ground‑truth annotations, ±50 ms tolerance, all 25 records
Figure 8. ground-truth precision / recall / F1
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
14
Notes: This is the decisive result: when checked against the dataset's actual annotated fetal QRS locations, the sequential analysis pipeline beats ICA on every axis — precision, recall, and F1 — by a wide margin (71.9% vs 56.2% F1). This is the clearest evidence supporting the paper's central claim, and it's why this metric (not the success-rate snapshot from the previous slide) is the headline comparison.

## Slide 15
Results III: FHR‑value accuracy (MAE/RMSE)
▪ Sequential Analysis: MAE 13.5 bpm / RMSE 17.4 bpm
▪ ICA: MAE 18.0 bpm / RMSE 22.2 bpm
▪ Estimated vs. ground‑truth FHR, all 25 records, common 1‑second grid
Figure 9. FHR-value accuracy
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
15
Notes: Beyond just matching QRS *locations*, this checks whether the resulting FHR *value* is actually close to the truth: both traces are interpolated onto a common time grid and compared point-by-point against the ground-truth FHR curve. Sequential analysis is noticeably more accurate on both error metrics, consistent with — and reinforcing — the precision/recall/F1 gap from the previous slide.

## Slide 16
Results IV: robustness to matching tolerance
▪ F1 recomputed at 10 / 25 / 50 / 75 / 100 ms ground‑truth matching tolerances
▪ Sequential Analysis leads ICA at every tolerance tested
▪ Confirms the ±50 ms headline result wasn't a cherry‑picked threshold
Figure 10. robustness to matching tolerance
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
16
Notes: A natural question about any single tolerance choice is whether it happens to favor one method. This sweep recomputes F1 across five tolerances from 10 to 100 ms for both methods — sequential analysis stays ahead of ICA at every single one, so the headline ±50 ms comparison on the earlier results slides isn't an artifact of that specific choice.

## Slide 17
Results V: signal quality drives reliability
▪ Dataset is genuinely hard: mean SNR ≈ −4.9 dB, mean SIR ≈ −12.0 dB
▪ Sequential analysis reliability degrades gracefully as SNR/SIR drop; ICA collapses more sharply — mirrors the paper's own finding
▪ Spearman ρ: SA–SNR 0.87 (p<0.001), SA–SIR 0.50 (p=0.012) — both significant; ICA–SNR 0.10 (p=0.63), ICA–SIR 0.18 (p=0.40) — neither significant
Figure 11. signal quality drives reliability
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
17
Notes: This scatter grid plots per-record reliability against the estimated SNR and SIR of each recording, for both methods. The sequential analysis method (top row) holds up reasonably well even as SNR/SIR fall, and this is statistically real: its reliability correlates strongly and significantly with both SNR and SIR. ICA (bottom row) is far noisier and drops to very low reliability more often in the same low-SNR region — and its correlation with SNR/SIR, while positive, is weak and not statistically significant at this sample size. This is exactly the robustness gap the original paper reported, now backed by the correlation numbers rather than just the visual trend.

## Slide 18
Discussion: why non‑blind wins, and where it struggles
▪ ICA assumes as many independent sources as channels — but real recordings have several MECG dipole components plus multiple independent EMG/motion sources plus the FECG
▪ Sequential analysis sidesteps this by exploiting known structure (periodicity, morphology) instead of blind independence
▪ Limitations, honestly: 7/25 records needed short NaN‑gap interpolation; a handful of records (a18, a09, a02, a11, a15) show markedly lower recall
▪ Consistent with the paper's own note: FECG amplitude is reduced around 28–32 weeks gestation (vernix caseosa)
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
18
Notes: ICA's independence assumption is fragile in this setting — there are simply more real interference sources than the 4 available channels can cleanly separate. Sequential analysis avoids that by using explicit domain knowledge at each stage. That said, be candid about limitations: a few records have real data-quality issues (short signal gaps) and a few show much lower recall than the rest, a pattern the original paper also links to gestational-age-dependent FECG amplitude loss.

## Slide 19
Conclusions
▪ Thesis supported on this dataset: non‑blind sequential analysis is both more reliable and more accurate against ground truth than blind ICA
▪ Gap is largest precisely where it matters most: low‑SNR/SIR recordings
▪ Practical relevance: viable direction for affordable, non‑invasive, potentially home‑based fetal monitoring
▪ Future work: reduced electrode montages, dynamic MECG windows accounting for heart‑rate‑dependent QT variation, improved fetal‑QRS detector for the low‑recall records
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
19
Notes: Bring it home: reproducing this method on a real, independently annotated dataset confirms the paper's central claim — a non-blind, a priori-informed pipeline outperforms blind ICA, especially under the low-SNR conditions typical of real abdominal recordings. Close with the practical motivation (affordable, non-invasive monitoring) and a few concrete next steps.

## Slide 20
Thank you / questions
▪ Thank you
▪ Questions?
Robust Fetal ECG Detection -- Sequential Analysis vs. ICA
20
Notes: Open the floor for questions.